EEG Recording and Analysis
For each group (withPCS and withoutPCS), 5 minutes of resting state with eyes open and 5 minutes of resting state with eyes closed were recorded using high-density EEG. EEG signals were recorded using a 128-channel EEG cap (128Ch Standard Brain Cap for actiCHamp Plus, Easycap GmbH, Wörthsee, Germany) with electrodes positioned in an equidistant layout, connected to an actiCHamp Plus amplifier (Brain Products GmbH, Gilching, Germany).
The sampling rate was 500 Hz with an amplitude resolution of 0.1 µV. Electrolyte gel was applied to improve conductivity between skin and electrodes, ensuring impedances remained below 20 kΩ. Eye movements and changes in the resting potential of the retina (EOG activity) were monitored using two EOG electrodes placed below each eye, with impedances also maintained below 20 kΩ. In addition, a ground electrode was positioned on the forehead, and a reference electrode was positioned on the tip of the nose. Impedances for both the reference and ground electrode were kept below 5 kΩ.

Preprocessing
Data preprocessing was performed using the FieldTrip toolbox (Fieldtrip-20240504; Oostenveld, Fries, Maris & Schoffelen, 2011) and the EEGLab toolbox (v2024.0; Delorme & Makeig, 2004) in Matlab (v24.1.0.2578822 (R2024a) Mathworks Inc., 2024, MathWorks® https://de.mathworks.com).
The participants' EEG data were organized in BIDS format (Pernet et al., 2019). Resting state EEG data were identified and imported into MATLAB for further processing. A trial defining function was built to select the data from the eyes-open condition for subsequent processing.
Filtering and Resampling
A finite impulse response (FIR) windowed-sinc (firws) filter was used for both high-pass and low-pass filtering on the continuous data. For high-pass filtering, a cut-off frequency of 0.1 Hz was applied to remove DC offset and low-frequency noise (slow drifts) (for accurate analysis). Low-pass filtering was performed with a cut-off frequency of 45 Hz to eliminate high-frequency noise and mitigate potential 50 Hz line noise.

A finite impulse response (FIR) windowed-sinc (firws) filter was used for both high-pass and low-pass filtering on the continuous data, (which ensures linear phase response and good frequency resolution). Initially, high-pass filtering was applied with a cut-off frequency of 0.1 Hz to remove DC offset and low-frequency noise (slow drifts) (for accurate analysis). Following the high-pass filtering, the data was downsampled from 1000 Hz to 250 Hz. This resampling step was conducted to reduce computational load while maintaining sufficient temporal resolution for subsequent analyses. (downsampling) reduce the data size for subsequent analysis. After resampling, low-pass filtering was performed with a cut-off frequency of 45 Hz to eliminate high-frequency noise and mitigate potential 50 Hz line noise (Delorme, 2023). Finally, the data underwent re-referencing using the Common Average Reference (CAR) technique to improve signal quality (Ludwig et al., 2009). As the name implies/suggests, an average of the recordings from all electrode sites is computed and used as the reference (Ludwig et al., 2009; Offner, 1950). Reref function was used. The data was converted into the EEGLAB data structure for further processing.
Artifact removal
After the initial filtering and resampling, the preprocessing pipeline continued with removing artifacts. First large artifacts (including the removal of flat-line channels, noisy channels, and short-time bursts of noise) were removed from the data using the EEGLAB pop_clean_rawdata function with specific parameters. Channels flat/Flat-line channels for more than 5 seconds were removed (FlatlineCriterion 5), channels poorly correlated with others were excluded (ChannelCriterion 0.85), data segments with abnormally high amplitude were eliminated (BrustCriterion 100), and time windows exceeding 0.4 standard deviations from the mean were discarded (WindowCriterion 0.4). Euclidean distance was used for similarity calculations, and the removals of high-amplitude data bursts were enabled. Again the CAR technique was applied to re-reference the data (after removing large artifacts), providing a more spatially uniform reference and minimizing the influence of the original reference electrode across all channels. This time, the EEGLAB pop_reref function was used/utilized. Secondly, Independent Component Analysis (ICA) (Bell and Sejnowski, 1995; Hyvärinen, 2013, Jung et al., 2000; Lee et al., 1999; Palmer et al., 2008) was performed on the data, to detect and reject further artifacts, such as eye or muscle movements (Makeig et al., 1995) using the pop_runica function implemented in EEGLAB. The runica algorithm was employed with the extended infomax option enabled. To avoid rank deficiency, the number of components was set to one less than the total number of channels (Kim, Luo, Chu, Cannard, Hoffman & Miyakoshi, 2023). This approach decomposes the EEG signal into independent components, potentially separating artifacts from neural activity. The resulting ICA weights, which represent the transformation matrix for this decomposition, were saved in a separate file.
Automatic component rejection was implemented using ICALabel. Thresholds were set at probabilities of 0.8 (80%) for muscle-related components and 0.5 (50%) for eye-related components. Components exceeding these thresholds were flagged and automatically removed using EEGLAB's pop_subcomp function. The two EOG channels (31 and 32) were removed from the dataset. The cleaned dataset was then checked for consistency using eeg_checkset. Thirdly and finally, an additional artifacts removed step was implemented to address any remaining problematic channels. This process involved a statistical approach to identify outlier channels based on their signal characteristics. The standard deviation and mean were calculated for each channel across all time points. Then, overall mean values for these standard deviations and means were computed across all channels. Thresholds were established at 2.5 standard deviations above and below the overall mean, creating an acceptable range for channel activity. Channels with standard deviations falling outside this range were identified as outliers. These outlier channels were then removed from the dataset using EEGLAB's pop_select function, further refining the EEG data quality. This step ensures that channels with unusually high or low variability, which might represent persistent artifacts or malfunctioning electrodes, are excluded from subsequent analyses.
Interpolate bad channels
Epoch length and number